RENSON LOUVRE SPECIFICATIONS

Brand		: LOUVRE PANEL

Type 		: 433 – SURFACE MOUNTED pressure-relief louvre

Manufacture and reference :

The 433 Louvre Panel is manufactured and supplied by Renson Fabrication Ltd.  Tel: 01622 754123

Email: louvres@rensonuk.net Website: www.renson.eu

Description:

RENSON 433 is an extruded aluminium louvre panel with pressure-relief/extractor hood blades mounted into an integrated frame. It is designed to be surface mounted onto a fixed structure. Pressure relief louvre blades open individually while extractor hood louvres open at the same time.

Dimensions/Size Range:

Minimum Height (mm)		228 (and a multiple of 100mm)

Length (mm)			800

Product Construction:

Profile: Extruded aluminium (EN 12020-2)

Surface Treatment:

Mill finish

Anodised (EV6/EV1) (20 micron): pre-treated and anodised.

Polyester powder coating in any RAL colour (40 micron): aluminium profiles pre-treated to resist corrosion to guarantee.

Installation:

Surface mounted using the screws and plugs that are provided.

Accessories

Stainless steel birdguard 6mm x 6mm secured to the rear

Stainless steel insect mesh 2.3mm x 2.3mm secured to the rear

Circular option available 433R

Product Information:

http://www.rensonuk.net/Louvres-panels-United-Kingdom.html