RENSON LOUVRE SPECIFICATIONS

Brand		: LOUVRE

Type 		: FLOOR GRILLE 311

Manufacture and reference :

The Renson 311 Floor Grille is manufactured and supplied by Renson Fabrications Ltd. Tel: 01622 754123

Email: louvres@rensonuk.net Website: www.renson.eu

Description:

RENSON 311 is a convector grille. Available with a flangeless ‘L’ frame - 311/1, flanged ‘Z’ frame – 311/2 or frameless 311/3.

System operation and Airflow Performance:

Type			311

Visual Free Area	76%

Physical Free Area	76%

Dimensions/Size Range:

Flange Height (mm)		14

Depth (mm)			25

Thickness (mm)		25

Pitch (mm)			16.5

Product Construction:

Profile: Extruded aluminium (EN 12020-2)

Surface Treatment:

Anodised (EV6/EV1) (20 micron): pre-treated and anodised.

Polyester powder coating in any RAL colour (40 micron): aluminium profiles pre-treated to resist corrosion to guarantee.

Installation:

Brackets 231 are available on request.

Accessories

Self-assembly kit

Product Information:

http://www.rensonuk.net/Louvres-panels-United-Kingdom.html