RENSON LOUVRE SPECIFICATIONS

Brand		: LOUVRE PANEL

Type 		: 521 – BUILT-IN 33mm pitch wall louvre

Manufacture and reference :

The 521 Louvre Panel is manufactured and supplied by Renson Fabrication Ltd.  Tel: 01622 754123

Email: louvres@rensonuk.net Website: www.renson.eu

Description:

RENSON 521 is a galvanised steel louvre panel. It is designed to be built into a pre formed opening. It can be supplied with or without a flanged frame.

System operation and Airflow Performance:

Type				521

Visual Free Area		68%

Physical Free Area		47%

Dimensions/Size Range:

Minimum Dimensions (mm)	300 x 300

Flange Height (mm)		40

Depth (mm)			43

Pitch (mm)			33.3

Product Construction:

Profile: Extruded aluminium (EN 12020-2)

Surface Treatment:

Mill finish

Anodised (EV6/EV1) (20 micron): pre-treated and anodised.

Polyester powder coating in any RAL colour (40 micron): aluminium profiles pre-treated to resist corrosion to guarantee.

Installation:

To be built into a reveal.

Product Information:

http://www.rensonuk.net/Louvres-panels-United-Kingdom.html