RENSON LOUVRE SPECIFICATIONS

Brand		: LOUVRE PANEL

Type 		: 423WK4 – BURGLAR-PROOF 50mm pitch wall louvre

Manufacture and reference :

The 423WK4 Louvre Panel is manufactured and supplied by Renson Fabrication Ltd.  Tel: 01622 754123

Email: louvres@rensonuk.net Website: www.renson.eu

Description:

RENSON 423WK4 is an extruded aluminium louvre panel using a burglar proof blade mounted into an integrated frame. It is designed to be built into a pre formed opening. It is supplied without a flanged frame.

System operation and Airflow Performance:

Type				423WK4

Visual Free Area		70%

Physical Free Area		22%

K-factor: Intake			27

K-factor: Discharge		27.1

Ce coefficient: Intake		0.193

Cd coefficient: Discharge	0.192

Burglarproof

Louvre 423WK4 is burglarproof according to class RC4, in accordance with EN1627 up to and including EN1630 (September 2011).

Dimensions/Size Range:

Minimum Dimensions (mm)	250 x 250

Depth (mm)			50

Pitch (mm)			50

Product Construction:

Profile: Extruded aluminium (EN 12020-2)

Surface Treatment:

Mill finish

Anodised (EV6/EV1) (20 micron): pre-treated and anodised.

Polyester powder coating in any RAL colour (40 micron): aluminium profiles pre-treated to resist corrosion to guarantee.

Installation:

To be built into a reveal. Stainless steel bars are to be incorporated into the wall. Reinforcing structure required for panels larger than 3m2.

Accessories

Stainless steel birdguard 6mm x 6mm secured to the rear

Stainless steel insect mesh 2.3mm x 2.3mm secured to the rear

Backframe, pre-installation frame, water channel, drainage channel

Product Information:

http://www.rensonuk.net/united-kingdom-wall-louvre-423-security-wall-louvre.html